## Slide 1: MODFLOW – Introduction Organization & Main Packages
CE EN 547 – BRIGHAM YOUNG UNIVERSITY

## Slide 2: Code Selection – Model Design
We are now at this spot in the model development process
MODFLOW is generally a safe and dependable choice for a model code
Model design = construction of numerical grid and model inputs

## Slide 3
Developed by McDonald & Harbaugh of the USGS, 1983
Public Domain
Most widely used groundwater model
Steady-state or transient saturated flow
Versions:
  MODFLOW 88
  MODFLOW 96
  MODFLOW 2000
  MODFLOW 2005
  MODFLOW-NWT
  MODFLOW-USG

## Slide 4: Finite Difference Model
3D Cartesian Grid
Cell-Centered

## Slide 5: Grid Geometry
Orthogonal in xy
Thickness varies in z

## Slide 6: Governing Equation
where:
Kxx, Kyy, Kzz = values of hyd. cond. along xyz axes
h = total head
W = Sources and sinks
Ss = Specific storage
t = time

## Slide 7: Processes & Packages
MODFLOW is divided into a series of processes & packages
Major tasks are organized as processes
More specific tasks are performed by packages
Each process may use one or more packages

## Slide 8: Global Process
Spatial discretization
  # rows, cols, layers
  Top/bottom elevations
Temporal discretization
  Stress periods
  Time steps
Units
Package Selection
Notes: There is a layer discretization file and a global package file that are used by the Global Process.

## Slide 9: Ground Water Flow Process
Formulation and solution of the ground water flow equation by the FD method
Main part of MODFLOW code
Includes
  Flow package (BCF, LPF, or HUF)
  Source/sink packages
  Solvers

## Slide 10: Observation Process
Used for model calibration
Calculates model-simulated heads and discharges to sources/sinks

## Slide 11: Required Packages
Discretization
Basic
Output Control
Flow Package (BCF, LPF, HUF, UPW)
Solver (SIP, SSOR, PCG, GMG, etc.)

## Slide 12: Optional Packages
CHB – Time Variant Specified Head
DRN – Drain
DRT – Drain Return Flow
ETS – Evapotranspiration Segments
EVT – Evapotranspiration
GAGE – Gage
GHB – General Head
HFB – Horizontal Flow Barrier
LAK – Lake
MNW – Multinode Well
MNW2 – Multinode Well 2
RCH – Recharge
RIV – River
SFR – Stream Flow Routing
STR – Stream-Aquifer Interaction
SUB – Subsidence
WEL – Well
UZF – Unsaturation Zone Flow

## Slide 13: Active/Inactive Zones
Cells outside problem domain are marked as inactive
Controlled by IBOUND array
(1=active, 0=inactive, -1=specified head)

## Slide 14: Virginia Coastal Plain Model
Notes: http://va.water.usgs.gov/online_pubs/WRIR/98-4085/g-wfmcpasys_va.html

## Slide 15: Flow Packages
Defines aquifer properties
Four options
  Block-Centered Flow (BCF)
  Layer Property Flow (LPF)*
  Hydrogeologic Unit Flow (HUF)
  Upstream Weighting (UPW), MODFLOW-NWT
*We will use the LPF package in this course

## Slide 16: LPF - Layer Property Flow Package
User enters Kh, Kv and storage terms for all layers
Kv can be entered as directly or in terms of vertical anisotropy
Horizontal anisotropy entered on a cell-by-cell basis
Two layer types
  Confined
  Convertible

## Slide 17: Well Package
Assigned to individual cells
Q can be steady state or transient
Extraction well (neg Q)
Injection well (pos Q)

## Slide 18: DRN - Drain Package
Assigned to individual cells
Used to simulate
  Agricultural drains
  Springs
  Creek beds
Required parameters
  Elevation
  Conductance

## Slide 19: Drains
Hijk
CD
Delev
Q = CD (Hijk - Delev) or
Q = CD (Delev - Hijk) for proper sign on Q
When the head is above the drain elevation:

## Slide 20: Drains
Hijk
CD
Delev
Q = 0
When the head is below the drain elevation:

## Slide 21: Conductance
Darcy’s Law:
where
q = flow rate
k = hydraulic conductivity
Dh = head difference
L = flow length
A = gross cross-sectional area

## Slide 22: Conductance, Cont.
Darcy’s law can be rewritten as:
where
The appropriate values for k, A, and L must be determined on a case-by-case basis

## Slide 23: Sample Conductance Calculation
Length of overlap of river on cell

## Slide 24: Recharge Package
One value assigned to each vertical column
Represents recharge due to precipitation
Can be steady state or transient
Infiltration rate must be assigned in correct units [L/T]

## Slide 25: Factors Affecting Recharge Rate

## Slide 26: Factors Affecting Recharge Rate
Rainfall
Runoff
  Slope
  Soil type
  Land use
Evapotranspiration
  Soil type
  Vegetation